# CR-CPU Instruction Set
## Introduction
The CR-CPU is a 16-bit general purpose programmable FPGA-CPU. It is intended to implement the minimal set of feature required to implement the C programming language.
## Registers
The CR-CPU contains four general purpose registers:
00: ra
01: rb
10: rc
11: rd
These registers are not fully interchangeable. Some instructions will require the use of certain registers.
## Instruction
Each instruction is a fixed 16-bits wide and is composed of the following components:
oooo aaaa cccc cccc
Where:
o = Opcode
a = Additional information
c = Constant
## Opcodes
The following opcodes are available:
0: Add (add)
1: Subtract (sub)
2: And (and)
3: Or (or)
4: Shift L/R (shfl, shfr)
5: Load (load)
6: Store (stor)
7: Move (mov)
8: Load Constant (loadc)
9:
A:
B:
C:
D:
E:
F:
## Additional Information
The additional information for an opcode is used to define the sub-command and/or the register(s) involved. Where possible, the first two bits are used to define the destination register for the result of the computation.