# CR-CPU Instruction Set
## Introduction
The CR-CPU is a 16-bit general purpose programmable FPGA-CPU. It is intended to implement the minimal set of feature required to implement the C programming language.
## Registers
The CR-CPU contains four general purpose registers:
00: ra
01: rb
10: rc
11: rd
These registers are not fully interchangeable. Some instructions will require the use of certain registers.
## Instruction
Each instruction is a fixed 16-bits wide and is composed of the following components:
oooo aaaa cccc cccc
Where:
o = Opcode
a = Additional information
c = Constant
## Opcodes
The following opcodes are available:
0: Add (add)
1: Subtract (sub)
2: And (and)
3: Or (or)
4: Shift L/R (shftl, shftr)
5: Load (load)
6: Store (stor)
7: Move (mov)
8: Jump (jmp, jifz, jinz, jgz)
9: Load Constant (loadc)
A:
B:
C:
D:
E:
F:
## Additional Information
The additional information for an opcode is used to define the sub-command and/or the register(s) involved. Where possible, the first two bits are used to define the destination register for the result of the computation.
## Opcode details
### Add (add)
Calculates the sum of two arguments (registers or constant) and places the result in a register.
ddxy
Where:
dd = Destination register (ra – rd)
x = Source 1 register (0: ra, 1: rb)
y = Source 2 register (0: rc, 1: constant)
### Subtraction (sub)
Calculates the difference between two arguments (source 1 – source 2) and places the result in a register. Uses the same encoding as add.
### And (and)
Performs bitwise “and” of two arguments. Uses the same encoding as add.
### Or (or)
Performs bitwise “or” of two arguments. Uses the same encoding as add.
### Shift L/R (shftl, shftr)
Performs a bitwise shift of a register. Note that zeros are always entered at the opposite end, even if the MSB is a one.
ddxy
Where:
dd = Destination register
x = Unused
y = Direction (0: right, 1: left)
### Load (load)
Loads a value from ram. The address of the location to load from is defined by the constant, and optionally, a register is added.
ddpp
Where:
dd = Destination register
pp = Offset pointer register (00: ra, 01: rb, 10: rc, 11: none)
### Store (stor)
Performs the inverse operation of the load command. Namely, stores the value contained in the “destination” register intro the memory location defined by the constant and the offset register. Uses the same encoding as load.
### Move (mov)
Moves (copies) a value from one register to another. The constant is unused.
ddss
Where:
dd = Destination register
ss = Source register (uses same encoding as destination register)
### Jump (jmp, jifz, jinz, jgz)
Optionally jumps to a new location. I.e. The instruction pointer is overwritten to a new value. “jmp” will jump unconditionally. The other will jmp if zero, if not zero, and if greater than zero respectively. Note that for the purpose of determining greater than zero, the value in the register is considered to be a signed value. The conditional jump instructions always uses the value in the rd register. This is because the rd register is less useful for other instructions. The location jumped to is determined by the sum of the pointer register and the constant.
ttpp
Where:
tt = Type of jump (00: jmp, 01: jifz, 10: jinz, 11: jgz)
pp = Pointer register (00: ra, 01: rb, 10: rc, 11: none)
### Load Constant (loadc)