CR-CPU Instruction Set
# Introduction
The CR-CPU is a 16-bit, general purpose, programmable FPGA-CPU. It is intended to be minimally complex while still being able to easily implement the C programming language. The CR-CPU uses a Von Neumann architecture which uses a common 64-bit bus for all peripherals and memory. The 64-bit bus contains 16-bits each of read address, read data, write address, and write data. The full 16-bit address space is usable for mapping.
# Instruction
The CR-CPU uses a fixed 16-bit width instruction set which contain 8-bits of opcode and operands, and an 8-bit immediate. Note that all instructions include the immediate, even if not required. The instruction is structured as follows:
oooo aaaa cccc cccc
Where:
o = Opcode
a = Additional information
c = Constant
The opcode encodes which operation should be executed, e.g. add, sub, jmp, call. See the Opcodes or Opcode details sections below for more details on each opcode.
The additional information section is used to define the sub-command and/or the operand(s) involved. Where possible, the first two bits are used to define the destination register for the result of the computation.
# Registers
The CR-CPU contains four addressable registers. Specifically, it contains two general purpose 16-bit registers:
00: ra	01: rb
The CR-CPU also has two special purpose 16-bit registers:
10: rp (pointer register)	11: sp (stack pointer)
The stack pointer register is implicitly used for all call, ret, push, and pop instructions. Note that the stack is assumed to start from a (user selected) high address and grows downwards. Also note that the stack pointer points to the last item pushed onto the stack. This means a push operation will first decrement the stack pointer, then write the value to the new location of the stack pointer.
The pointer register is a special register which, in addition to being usable as a general purpose register, is usable as an offset for load and store operations. It is therefore excellent for use as a pointer register, or to keep track of an offset into an array.
The CR-CPU also contains an additional 8-bit address register. Since all instructions only include an 8-bit constant which is insufficient to directly address the entire memory space, the address register may be loaded with the high 8-bits of the address to be used in a memory operation or a jump/call operation. This gives a total address space of approximately 64k words for program and memory. This is more than the CR-CPU can contain on current hardware but could be used for future expansion or memory mapped peripherals.
# Reference
0	0000
1	0001
2	0010
3	0011
4	0100
5	0101
6	0110
7	0111
8	1000
9	1001
A	10	1010
B	11	1011
C	12	1100
D	13	1101
E	14	1110
F	15	1111
# Opcodes
The following is a summary of the opcodes available:
0: Add (add)
1: Subtract (sub)
2: And (and)
3: Or (or)
4: Xor (xor)
5: Shift L/R (shftl, shftr)
6: Load (load)
7: Store (store)
8: Move (mov)
9: Jump (jmp, ifz, inz, gz), relative jump
A: Load immediate (loadi, loadi.h)
B: Push, pop
C: Call, relative call, ret
D: Load address (loada)
E: Halt
F: No operation (nop)
# Opcode details
## 0x0: Addition (add)
Calculates the sum of two arguments (registers or constant) and places the result in the first register. Note that in the case of the constant, it is zero extended.
ddss
Where:
dd = Destination and source 1 register (00: ra, 01: rb, 10:rp, 11:sp)
ss = Source 2 register (00: ra, 01: rb, 10:rp, 11:constant)
## 0x1: Subtraction (sub)
Calculates the difference between two arguments (source 1 – source 2) and places the result in the first register. Uses the same encoding as add.
## 0x2: And (and)
Performs bitwise “and” of two arguments. Uses the same encoding as add.
## 0x3: Or (or)
Performs bitwise “or” of two arguments. Uses the same encoding as add.
## 0x4: Xor (xor)
Performs bitwise “xor” of two arguments. Uses the same encoding as add.
## 0x5: Shift L/R (shftl, shftr)
Performs a bitwise shift of a register. Note that zeros are always entered at the opposite end, even if the MSB is a one. Note that since the registers are 16-bits wide, only the bottom four bytes rb or the constant are used as the shift amount.
ddsy
Where:
dd = Source and Destination register
s = Shift amount source (0: rb, 1: constant)
y = Direction (0: right, 1: left)
## 0x6: Load (load)
Loads a value from RAM or peripheral. The load address may be defined in one of two ways: as an absolute address, or as a relative address. In the case of a relative address, the load address is defined by the sum of the signed immediate plus the pointer register or stack pointer. In the case of an absolute address, the load address is defined by the address register as the high byte and the constant as the low byte.
ddpp
Where:
dd = Destination register
pp = Offset selection (00: rp, 01: sp, 10: address, 11: unused)
## 0x7: Store (store)
Performs the inverse operation of the load command. Specifically, stores the values of the given register into the given address. See load entry on how to compute the address.
## 0x8: Move (mov)
Moves (copies) a value from one register to another. The constant is unused.
ddss
Where:
dd = Destination register (00: ra, 01: rb, 10: rp, 11: sp)
ss = Source register (00: ra, 01: rb, 10: rp, 11: sp)
## 0x9: Jump (jmp)
Optionally jumps to a new location. I.e. The instruction pointer is overwritten with the new value. There are three mutually exclusive, optional flags. Specifically:
z = Jump if ra is zero
nz = Jump if ra is non zero
gz = Jump if ra is positive (specifically, if the most significant bit is zero)
For relative jumps, the instruction constant is considered to be signed and is added to the current instruction pointer, therefore the jump range is +127 .. -128. Relative jumps are selected using the “r” flag. For absolute jumps, the address is the address formed by the address register for the high byte and the instruction constant for the low byte.
ttrx
Where:
tt = Type of jump (00: jmp, 01: jifz, 10: jinz, 11: jgz)
r = Absolute vs relative jump (0: relative, 1: absolute)
x = Unused
## 0xA: Load Immediate (loadi)
The load immediate instruction can be used to load a constant directly from an instruction to a register. Since the constant is only 8 bits and the registers are 16 bits, it provides options to load the low or high byte.
ddtx
Where:
dd = Destination register
t = Type of load (0: low byte, set high byte to zero, 1: high byte, leave low byte untouched)
x = Unused
## 0xB: Push, Pop (push, pop)
The behaviour of the opcode depend on which sub-command is used. Note that the stack pointer points to the last pushed item on the stack.
push = Pushes an item onto the stack. Specifically, decrements the stack pointer and then writes to the new location of stack pointer.
pop = Pops an item into a register from the stack. Specifically, returns the value at the location of the stack pointer, and then increments the stack pointer. Note if the value being pop-ed is unneeded, then it is more efficient to add 1 to the stack pointer (1 clock) than it is to pop into an unused register (2 cycles).
ddxt
Where:
dd = Source register
x = Unused
t = Type of operation (0: push, 1: pop)
## 0xC: Call, Return (call, ret)
This instruction performs various function related tasks depending on the sub-command. Note that for the call instruction, the addressing is identical to the jump instruction.
call = Performs a function call using an absolute address. For the address, the address register is used for the high byte, and the instruction constant is used for the low byte. Specifically, this instruction will push the current instruction pointer plus one onto the stack, and then jump to the given address.
call.r = Performs a relative function call. The destination address is the sum of the sign extended instruction constant and the current instruction pointer. Specifically, this instruction will push the current instruction pointer plus one onto the stack, and then jump to the given address.
ret = Performs a return from a function. Specifically, pops the top stack location into the instruction pointer, effectively jumping to that location.
xxrc
Where,
xx = Unused
r = Absolute vs relative call (0: relative, 1: absolute)
c = Type of operation (0: call, 1: ret)
Effectively: 00: rcall, 01: ret, 10: call, 11: ret
## 0xD: Load Address (loada)
Loads the 8-bit address register with the instruction constant in preparation for a load, store, jmp, or call. No additional information is used for this instruction.
## 0xE: Halt (halt)
Halts the processor. No additional information is used for this instruction.
## 0xF: No Operation (nop)
Performs no operation. It takes one clock and can therefore be used by the programmer for timing control. No additional information is used for this instruction.
# CR-CPU assembler
An assembler is provided to convert assembly written for the CR-CPU to binary which can then be run on the CPU. The assembler has a number of features which allow the programmer to easily write assembly programs, e.g. static variable allocation, named constants, and automatic relative and absolute jump address calculation.
## Assembler directives
Assembler directives can be used by the programmer to inform the assembler of some piece of information. In general the directives do not generate any output on their own. The following directive are available:
### Instruction Label
A label stores the location of the next instruction generated at assembly time. This can then be used in jump and call instructions to set the offset. When labels are defined they must follow the format “.label_text:”, i.e. with a leading period and a trailing colon. They must be on a line by themselves. When they are referenced in instructions they must follow the format “.label”, i.e. leading period but not trailing colon. Note that labels are stored as 16-bit values but only either the upper or lower byte is used as the constant for the instruction depending on the context (since all instructions include an 8-bit immediate). E.g. “loada” and “loadi.h” use the upper byte, while “loadi” and “call” use the lower byte. For example:
nop	# arbitrary number of instructions here, in this case one
.loop:	# creates a label on the next instruction, in this case instruction one
add ra, 1
jmp.nz .loop	# jumps to the label “.loop”, in this case equivalent to jmp.nz 0x01
Another example:
loadi ra, 10
loadi rb, 20
loada .fn_add # note that the high byte of .fn_add is used here
call .fn_add # note that labels can be referenced before they are defined
store ra, .output_addr # note that the correct relative address is generated automatically
.... # more code
.fc_add: # will jump here when call is executed
add ra, rb
ret
### Constants
Constants are similar to labels, except the programmer can directly supply their value. Note that like labels, constants are always of type unsigned 16-bit integer. Similar to labels, either the low or high byte will be used automatically depending on context. Constants are great for defining the addresses of memory mapper peripherals so that they can be changed easily in the future. For example:
.constant 0xabcd my_const
loadi ra, .my_const # loads ra with 0x00cd
loadi.h ra, .my_const # upper byte of ra is 0xab while leaving the lower byte unchanged
Note that similar to static variables below, an assembly time offset can be added to a constant. This constant will roll over into the high byte where required. For example:
.constant 0x20FF my_const
loadi ra, .my_const[2] # loads ra with 0x0001
loadi.h ra, .my_const[2] # loads the high byte of ra with 0x21 (forming 0x2101)
### Static Variables
Definition of a static variable performs two operations: it places initialization data of the variable into the machine code, and it creates a label which can be used in the same way as described above. Static arrays or structs may also be defined by using a size other than 1. If no initialization data is provided, then the variable will be initialized with zero. If initialization data is provided, it must be provided for every member of a variable. Space for static variables is created after the code section of the executable. The offsets of all variables are calculated during assembly. For example:
.static 1 var_a # simple var of 16-bits, initialized to zero
.static 1 var_b 0xAFEB # simple var with an initialization value
.static 3 var_c 10 11 13 # static array with non-zero initialization
loadi rp, .var_a
loadi.h rp, .var_a # these two instructions load the ADDRESS of var_a into rp
load.rp ra # loads the value of .var_a into ra
Alternatively,
loada .var_a # loads the high byte of the address of var_a
load ra, .var_a # loads value from variable var_a
For arrays,
loada .var_c[2]
load ra, .var_c[2] # loads from address var_c + 2, i.e. value 13
### Comments
Comments may be placed in the assembly code. Any text which is preceded by a “#” will be ignored by the assembler. This includes both on the same line as an instruction or on a line by itself. For example:
# this is a line comment
loadi ra, 0 # this comment is on the same line as an instruction
### Text Offset
The “.text_offset” assembler directive allows the programmer to specify to the assembler that the program should be built to run at a location other than 0x0000 in memory. This is useful, for example, if the OS is loaded at 0x0000 .. 0x00FF and the program to be run will be loaded at 0x0100. This offset will be applied directly to the .text section. It is also applied to the .data section since it is after the .text section. The directive may appear anywhere in the program.
# example
.text_offset 0x0100
## Examples of instruction usage
### Add, sub, and, or, xor
These arithmetic instructions all use the same format. Specifically, they take two operands, the first is a register which is both the first source and the destination and second which can be either a second register or a constant (immediate). Note that the second register cannot be sp. For example:
add ra, 1 # add an immediate to a register
add ra, rb # add two registers
add rb, .label # add the value of a label to a register
Labels may be a constant, instruction location, or static variable location.
### Shftr, shftl
Similar to arithmetic instructions, shift instructions take a destination register which is also the first source register. However, the second operand may only be one of rb or an immediate.
Example usage:
shftl ra, rb # shift by an amount in rb (note only low 4 bits are used)
shftl rb, 2 # shift by a constant (must be 0 .. 15)
shftr ra, 3 # same but shift right
### Load, store
The load instruction takes two operands and an optional set of flags. The first operand is the destination register. The second is an immediate. Optionally, the rp or sp flag can be given to specify to load relative to one of those registers. If not, then the load is performed relative to the 8-bit address register. Store follows an identical structure, except that the first operand instead is the source, rather than the destination.
Example usage:
load 0x81
load ra, 0x20 # loads ra with the value from addres 0x8120
load.rp ra, 1 # loads from rp + 1
load.sp rb, 2 # loads from sp + 2 (ex. for accessing stack arguments)
store.rp rb, 0x10 # stores the value from rb into the location of rp + 0x10
### Mov
The move instruction has a single format, which has a destination operand and a source operand. For example:
mov ra, rp # moves contents of rp to ra
### Jmp
The jump instruction handles both conditional and unconditional jumps. The condition is chosen by using an optional flag. This flag may be one of “z”, “nz”, or “gz” to specify “if zero”, “if not zero”, or “if greater than zero”, respectively. Note that there are no status flags in the processor, the condition is always evaluated on the contents of the ra register. The address to be jumped to can either be specified absolutely or can be specified relative to the current address. In the case of relative addresses, the assembler will calculate the offset for you. Relative jump can be specified using the “r” flag. In the case of a relative jump, the target of the jump must be in the range -128 .. 127. For example:
jmp.r .label # unconditionally jump to .label
In the above case, the relative offset between the jump instruction and the label is calculated at assembly time. Note that the order of the condition and relative flag does not matter.
jmp.nz.r .label # conditionally jump if the ra register is non-zero
jmp.gz.r .label # conditionally jump if the ra register is positive, i,e, if the MSB is zero
In the case of an absolute jump, i.e. a long jump, typically the upper byte will first be specified in the address register and then the lower byte will be specified in the immediate of the jump instruction. For example:
loada 0x71
jmp.z 0x23 # jumps to address 0x7123 is ra is zero
Of course, example above could have used a label instead.
### Loadi
The load immediate instruction loads the immediate from the instruction into either the low or the high byte of the destination register. In the case of the low byte is selected, the high byte is set to zeros. In the case of the high byte, the low byte is kept unchanged. This allows the programmer to set the whole value of a register with a single load if the value is in the range 0x00 .. 0xFF. Or all bytes in the register can be set by setting the low byte first and then the high byte. For example:
loadi ra, 0xCD # loads ra with the value 0x00CD
loadi.h ra, 0xAB # loads the high byte of ra with 0xAB
If the two above commands were performed in sequence, then ra would contain the value 0xABCD. This instruction can also be used to load the value of a constant:
.constant 0xBEAF const # no code gen, just creates the label
loadi ra, .const
loadi.h ra, .const # ra is now loaded with the value 0xBEAF
Or can be used to load the address of a static variable. This is useful to load the address into rp where it can then be used as an offset pointer to load and store.
.static 256 my_array
loadi rp, .my_array
loadi.h rp, .my_array # rp now contains the address of my_array
Note that since static data is allocated after the text (code) segment, the address of the variable is unknown to the programmer and is only calculated at assembly time. The rp register loaded above can then be used as follows:
load.rp ra, 10 # load ra with the tenth element in my_array
add rp, 1 # increment rp to walk through the array
load.rp ra, 0 # deference at the location of the pointer by using offset zero
add rp, 1 # walk again to the next element
load.rp rb, 0 # load rb with the next (now third) element of the array
### Push, pop
The push and pop instructions perform identical but opposite actions. Both take a single operand, the register which is used as the source in the case of push, or the destination in the case of pop. The push and pop instruction add or remove an item from the top of the stack, as defined by the stack pointer (sp). Note that the stack pointer pointer points to the first empty location on the stack. Note that the stack grows from high addresses to low addresses. For example:
push ra # write ra to the address sp and subtracts one from sp
pop rb # adds one to the stack pointer then reads the value
add sp, 1 # equivalent to pop, except only one cycle and the value is not read
sub sp, 10 # allocates 10 new spots on the stack that can be used for local variables
### Call
The call instruction is used to call functions. Mechanically, it pushes the program counter onto the stack and then unconditionally jumps to the location specified. The location can be either absolute or relative. In the case of absolute, the upper byte is taken from the address register and the lower byte is taken from the immediate. In the case of relative, the offset is taken only from the immediate. For example:
loada 0xEF
call 0xAB # will jump to the location 0xEFAB
Of course typically labels will be used:
.... # load ra and rb with appropriate values
loada .func
call .func
.... # more code
.func:
add ra, rb
ret
In the case of relative function calls, the call can be made directly without needing to set the address register first. The assembler will automatically generate the correct relative offset between the call and the function.
.... # load ra and rb with appropriate values
call.r .func
.... # more code
.func:
add ra, rb
ret
### Ret
The ret instruction is placed at the end of a function definition. When it is executed, it pops the top value of the stack and performs an unconditional jump to that location. It is therefore critical that any values pushed onto the stack have been pop-ed off before the ret instruction is executed. For example:
.my_func:
sub sp, 10 # allocate local storage
....
store.sp ra, 5 # use that storage
....
add sp, 10 # sp must be restored before ret is executed
ret
### Loada
Loada is used to set the 8-bit address register. The value of the immediate is loaded directly into this register. In the case where the immediate is a label (const, static var address, text label), the high byte of the value will be used by the assembler. For examble
loada 0xDE # address register now contains 0xDE
.constant 0xABCD const
loada .const # address register now contains 0xAB
### Halt
The halt instruction takes no operands. When it is executed the processor will stop and will no longer fetch or process instructions.
### Nop
The nop (no operation) instruction performs no action except take one cycle. They have no effect on the computation and can be used anywhere in the instruction stream. They could be used if an exact number of cycles needs to be waited.
## Recommended calling conventions
Since the assembler does not handle calling conventions, no particular calling convention must be followed. However, for compatibility with future compilers and for uniformity, the following calling conventions are recommended.
### Function argument location
Arguments to function should be first in ra, then rb, then on the stack where the rightmost argument is pushed first. This means that inside a function body the arguments 2 through n are accessible from sp+1 to sp+(n-1) (the return address is stored at sp+1).
### Caller vs Callee saved registers
All registers which are not used by function arguments must be saved (as required) by the callee. Thus if a function which takes a single argument (in ra) wants to use rb, then it must first save the value of rb, and must restore the value of rb before returning. Note that the typical way of implementing this is to push rb at the beginning of the function and pop it at the end.
There is one exception to this, the 8-bit address register. This register is not expected to hold its value across a function call. This is because there is no way to save and load the address register.
### Return value is return in ra when required
When a return value is specified, it will be placed in ra before returning from the function. In functions which take an argument in ra but do not return anything, the value left in ra is unspecified. In functions which do not take arguments and which do not return anything, the value of ra should persist across the function call (as any other register).